Simplify							Expand

1)	6a4b3 x 2ab7 = 				6)	m(2m2 – 5) =

2)	(3ab4)2 =						7)	-4p2(2p4 + 3) =

3)	12m4n5  6mn5 = 			8)	-2p(2q – 5)3 =

Factorise

4)	(2a2b)4 x 4a5 =				9)	24m3e4 – 32e5 =

5)						10)	  16m3n – 20m6n8 =

. Factorising: What do you notice? .

1) 		2 × 3 = 6   Factors 1,6   2,3

2) 		-5 × 12 = -60     Which add to -17?

Factors 1,-60   2,-30   3,-20   4,-15   5,-12   6,-10

. Factorising: What else do you notice? .

1)

2) 		25 × 4 = 100,        Factors of 100 = 10,10

3)

4)

5)

eg 7x2 + 13x – 2

7x2 + 13x – 2

Multiply the number in front of x2 and the constant    7 × -2 = -14

List the factors of this number    Factors of -14  =  1 × -14    -1 × 14

2 × -7      -2 × 7

Which pair add to +13   (number by the x)                +14 and - 1

Rewrite the question splitting the middle term         7x2 + 13x – 2

7x2 + 14x – 1x – 2

Factorise each pair                                               7x(x + 2)  – 1(x + 2)

Factorise again                                                     (7x – 1)(x + 2)

Try these

1)  5x2 + 11x + 2 			2) 4x2 + 21x + 5 				3) 3x2 – 7x – 6

Factorise these quadratics:

1) x2 – 6x + 9 = 						3)  9x8 – 42x4y5 + 49y10  =

2) 4x2 – 12x + 9= 					4)

Expand (2x + 3)(2x – 3) =									extension:

So factorising these is easy								x2 – 3y + xy – 9

1)  x2 – 16 = 							4)  4x2 – 4 =

2)  9x2 – 49y2  = 						5)  9x2 –  =

3)  4x4 – 121y6  = 					6)  x2 – y2 =

Algebra fractions can sometimes be simplified by factorising first

Factorise as much as possible and cancel

1) 					2)

3)  					4)

5)

6)

# Text boxes

=1

Is there a difference between squares?

eg  4x4 – 9y2

Theta

Ex 3.06

Harder Factorising

Perfect squares

Theta

Ex 3.07

Factorising and cancelling

Yes

Factorise by parts

= x(y + 3) + 2( y + 3)

= (x + 2)(y + 3)

Difference between two squares

No

Theta  Ex 3.05

1)

2)

3)

4)

Factorise by basic method

eg x2 + 3x + 2

= (x + 2)(x + 1)

No

Ex 3.05

Factorising & fractions

Factorise

(2x2 – 3y) (2x2 + 3y)

HW Theta pg 14

Harder factorising method

2x2 + 11x + 5

= 2x2 + 10x +1x + 5

= 2x(x + 5) + 1(x + 5)

= (2x + 1)(x + 5)

Yes

Ex 3.06

What is there a coefficient in front of x2

eg  2x2 + 11x + 5

Factorise out the common factor first

4(x2 + 3x + 2)

Not 1

Factorising Review

5)

6)

7)

8)

9)

Achieve!

Yes

No

Are there 4 terms (in two pairs)?

eg xy + 3x + 2y + 6

Is there a common Factor?

eg 4x2 + 12x+ 8

Achieve!

Starter

Ex 3.07

HW Theta pg 13 Done?

Ex 3.06